## Slide 1
Digital Twin Architecture and Data Flow
ROBOT (each of 2) · Jetson Orin NX 16 GB · ROS 2 Humble
SERVER · workstation with RTX GPU · ROS 2, Isaac Sim, Sionna RT
network
Sensors + robot
Ouster LiDAR · 10 Hz
IMU · 100 Hz
Drive base
RGB-D camera
Wheel enc. (backup)
Radio antenna
Start + odometry
FAST-LIO2
LiDAR-inertial IEKF · ATE 2.0–4.4 cm
fallback RKO-LIO · cuVSLAM 23–47 cm
Board start
ChArUco → initial guess in map
detection online: to build
Map localization
offline equivalent: 1.3 cm
Fused pose
FAST-LIO2 odometry · map→odom
10 Hz, map frame, bounded error
map→odom (one owner)
in map: scan-to-map on map tiles, 1–2 Hz
outside: server SLAM correction
server lost: peer Swarm-SLAM
Link to server
rates estimated
↑ Keyframe packs
scan + JPEG + pose · ~2 Hz · 0.5–1 MB/s → SLAM
↑ Map-frame pose
fused pose · 10 Hz · ~1 KB/s → robot prims
↓ Map tiles
twin map + new SLAM areas + scene edits · 1–5 MB, rare
↓ SLAM corrections
keyframe ID + pose · ~10 s · <100 B · outside map
↓ Control commands
from Isaac Sim / operator → drive base
↕ Peer (robot j)
Swarm-SLAM descriptors, scans · server lost only
Robot j
same stack · peer Swarm-SLAM
Clock sync
PTP / chrony: robots, server, sniffer
odometry
initial guess
Multi-Agent SLAM
centralised
Map store
keyframe packs in;
tiles + corrections out
Swarm-SLAM
inter-robot + map
→ SLAM corrections
Live mapping
GPU
Splat mapper
Gaussian-LIC
ROS 2 port
Live map
Gaussian splats
+ LiDAR points
Scene update
Decomposition
segments, materials
maintenance: prune, reuse
Object retrieval
PE keyframes, SAM 3 mask
depth, LiDAR scale/offset fit
fused cloud, cached per keyframe
Change detection
live scans vs current twin
free-space carving
live map
Offline twin
versioned
Twin update
re-run on stored keyframe packs
GLIM + BA
GLIM map, board check: 4 mm
Anchored map
reference ~1.3 cm · version n
LOD-3DGS + mesh
twin splats, radio mesh
Isaac Sim
USD stage
Robot + antenna prims
one per robot, map-frame pose
every frame
Semantic layer
class + instance ID per prim
from scene update
Gaussian layer
twin splats + live map
RTX visuals
Mesh layer
physics, radio materials
USD edits
classes, IDs
splats, mesh
Sionna RT
Scene export
USD to Mitsuba scene
Path solver
all Tx/Rx links
Channel output
CIR per link, radio map
Validation
measured CSI / RSSI (sniffer)
vs simulated channel
meshes, materials, all Tx/Rx poses
expected view
robot hardware
SLAM, mapping
scene update
offline, per site
simulation
radio
network: robot ↔ server and robot ↔ robot
not built yet
one map→odom owner at a time; server takes over on reconnect
10/40