## Slide 1
SCooP-iT Testbed Questions
A testbed paper is judged on seven questions
  Trust: can readers rely on the instrument?
    Q1 Precise. Are its own errors small next to the effects it measures? (E1 Headroom)
    Q2 Consistent. Do the poses and the link logs agree when neither was checked by hand? (E2 Map Meets Radio)
    Q3 Faithful. Does replaying a logged link reproduce what the live link did? (E3 Twin Run)
    Q4 Repeatable. Does the same setting give the same link on another day? (E4 Same Knob, Same Link)
    Q5 Necessary. What does a measured link show that a synthetic one hides? (E5 Sim Gap)
  Worth: should anyone care?
    Q6 Unique. What can it do that no existing platform can?
    Q7 Reproducible. Can someone else build and use it?
  Pass criteria fixed before the data were read; answers from the 24 Sep session (mapping_A, survey_1, coop_2)
1/14

## Slide 2
Q1. Is it precise?
Are the testbed's own errors small next to the effects it measures?
  If clock or pose errors were as coarse as the effects under study, every later number would be ambiguous. Pass: each term 10x below the breaking point of its kind (0.2 m pose; one LiDAR frame for time)
  Q1.1 How far apart are the agents' clocks?
      Setup: chrony offset logs over coop_2, turned into displacement at 1 m/s
      Answer: 0.99 ms measured = 1 mm, 101x below one frame; strict bound 12 ms = 1.2 cm, 8x (short)
  Q1.2 How well is an agent without LiDAR placed in the LiDAR frame?
      Setup: held-out ChArUco boards predict where the board should appear; map built once, frozen
      Answer: RGB-D cart 3.1 cm median (6.5x below 0.2 m, short of 10x); LiDAR robot 10 mm (coop2_0828); map repeats to 1.06 cm
      Lacking: LiDAR robot vs boards on coop_2; radar and LiDAR-camera residuals; sniffer bias; measured p95 speed; rangefinder control distances
2/14

## Slide 3
Q1 results: is it precise?
Term | Pass | Value | Margin
Answered |  |  | 
Clock offset, measured | coop_2 | 0.99 ms (1 mm at 1 m/s) | 101x, pass
Clock offset, strict chrony bound | coop_2 | 12 ms (1.2 cm) | 8.3x, short
Map refinement, final correction | mapping_A | 0.15 cm, 0.017 deg | 133x, pass
Map repeatability, four weeks apart | two maps | 1.06 cm, scale 2e-5 | 19x, pass
Board detector vs pipeline | mapping_A | 8.1 mm ZED, 8.3 mm RealSense | 24x, pass
RGB-D cart vs held-out boards | coop_2 | 3.1 cm median, sigma 5.3 cm | 6.5x, short
LiDAR robot vs held-out boards | coop2_0828 | 10.0 mm, 0.88 deg | 20x, pass
Still needed |  |  | 
LiDAR robot vs boards on coop_2 | coop_2 | board_table.py | 
Radar and LiDAR-camera extrinsic residuals |  | held-out reflector positions and boards | 
Sniffer clock bias |  | probe stamps or field session | 
Measured p95 agent speed |  | reference tracks (headroom.py --traj) | 
Control distances, map minus rangefinder |  | per site | 
3/14

## Slide 4
Q2. Is it consistent?
Do the poses and the link logs agree when neither was checked by hand?
  The map and the poses never saw the radio; the radio never saw the map. If map geometry predicts the signal, both are validated at once
  Q2.1 Does Fresnel clearance through the map predict RSSI?
      Setup: per 0.5 s window, clearance of the link path through the anchored map vs RSSI with the distance trend removed (fixed exponent). Pass: rho > 0.3 and clear-minus-obstructed drop > 5 dB
      Answer: mobile_2 CSI link rho 0.60, 5.4 dB: pass. infra_1 link rho 0.23, 4.7 dB: short. Self-test recovers a planted 12 dB wall as 11.9 dB
  Q2.2 Does it hold on the links the benchmark replays?
      Setup: agent-to-access-point RSSI and goodput, pooled over survey_1 and coop_2
      Lacking: AP position in the map (ap.yaml); pooled rho with a confidence interval; out-of-run prediction (fit survey_1, score coop_2); CSI power as second signal
4/14

## Slide 5
Q2 results: is it consistent?
Link | Pass | rho, drop | Verdict
Answered |  |  | 
mobile_2 to sniffer, CSI | coop_2 | 0.60, 5.4 dB | pass
infra_1 to sniffer, CSI | coop_2 | 0.23, 4.7 dB | short
Method self-test, planted 12 dB wall | synthetic | 0.68, 11.9 dB recovered | pass
Still needed |  |  | 
Agent to access point, RSSI and goodput | survey_1, coop_2 | AP position in ap.yaml | 
Pooled over passes and sites |  | link_clearance.py --all | 
Confidence interval on rho |  | bootstrap over windows | 
Out-of-run prediction |  | fit survey_1, score coop_2 | 
CSI power as second signal |  | column present, untested | 
5/14

## Slide 6
Q3. Is it faithful?
Does replaying a logged link reproduce what the live link did?
  Replay is what the testbed offers every method. If replay does not match reality, the logged channel is just another simulation. This is the headline claim
  Q3.1 Do replayed arrivals match live arrivals?
      Setup: twin runs on the survey_1 route: run A logs the link (iperf, ping); run B sends stamped 1 KB / 100 KB / 1.5 MB messages at 10 Hz. Replay B through A's trace: arrival = send + d(t) + s/G(t), dropped in outage
      Pass: at least 90 % agreement on which 100 ms frame each message lands in, and closer than the synthetic channel
      Answer: none yet. The model and its measured inputs (goodput, RTT, outages) exist; no live messages to compare against
      Lacking: payload node; one session (A1/B1 survey, A2/B2 cooperation, back to back); twin_run.py; per-size, per-mode table of arrival error, frame agreement, drop agreement
6/14

## Slide 7
Q3 results: is it faithful?
Item | Status | How
Answered |  | 
Replay model d(t) + s/G(t), drop in outage | defined | one module, three channels
Inputs: goodput, RTT, outages | measured | every pass
Live arrivals to compare against | no data | none recorded
Still needed |  | 
Payload node, 1 KB / 100 KB / 1.5 MB at 10 Hz | to write | ROS 2 pub/sub, stamps both ends
Twin runs A1/B1 survey, A2/B2 cooperation | one session | survey_1 route, same day
Arrival error, frame agreement, drop agreement | to compute | twin_run.py; pass >= 90 % frame agreement
7/14

## Slide 8
Q4. Is it repeatable?
Does the same setting give the same link on another day?
  A testbed setting is useful only if it repeats; otherwise "cooperation mode" is not a controlled condition
  Q4.1 Does the frame repeat?
      Setup: two maps of the same site, four weeks apart, processed independently
      Answer: 1.06 cm wall placement, scale within 2e-5
  Q4.2 Does the link repeat?
      Setup: Wasserstein and KS distance on RTT, goodput, RSSI (and RSSI on shared map cells) between two days of one mode, against the distance between survey and cooperation mode. Pass: day/mode ratio below 0.5
      Answer: untested. Mode distance (survey_1 vs coop_2) computable from data in hand: link_repeat.py
      Lacking: run link_repeat.py on survey_1 vs coop_2; one repeat day on the same route (the Q3 session provides it); day-vs-mode table
8/14

## Slide 9
Q4 results: is it repeatable?
Half | Pass | Value | Verdict
Answered |  |  | 
Frame across days | two maps, 4 weeks | 1.06 cm, scale 2e-5 | pass
Link across modes, same day | survey_1 vs coop_2 | computable | untested
Link across days, same mode | needs repeat |  | untested
Still needed |  |  | 
Mode distance |  | link_repeat.py survey_1 coop_2 | 
Repeat day, same route and modes |  | from the Q3 session | 
Day-vs-mode ratio, RTT and goodput |  | link_repeat.py --against; pass < 0.5 | 
9/14

## Slide 10
Q5. Is it necessary?
What does a measured link show that a synthetic one hides?
  Every collaborative-perception benchmark models the channel synthetically: constant or i.i.d. delay, quantized to whole frames, no outages. If that described the real link, nobody would need to measure it
  Q5.1 How much benefit is left when everyone talks at once?
      Setup: 1.5 MB messages at 10 Hz through the logged link, delay = RTT/2 + size/goodput, lost in outages; one sender (survey_1) vs two robots (coop_2); synthetic channels as configured in their code
      Answer: within one LiDAR frame: 86 % alone, 59 to 68 % crowded, 100 % under V2X-ViT (constant 100 ms) and Where2comm (no latency); RTT 5 to 10 ms idle, 25 to 33 ms loaded; 3 real outages, 12 % of frames (coop2_0828)
  Q5.2 Would a tuned synthetic channel do?
      Setup: constant or Binomial delay fitted to the measured delays; same in-frame share
      Lacking: best-fit synthetic baseline; more passes and a second site; probe-off control run (iperf itself loads the link)
10/14

## Slide 11
Q5 results: is it necessary?
Quantity | Pass | Value | Verdict
Answered |  |  | 
1.5 MB in frame, one robot | survey_1 | 86 % | shown
1.5 MB in frame, two robots contending | coop_2 | 59 to 68 % | shown
1.5 MB in frame, synthetic channels | code | 100 % (V2X-ViT 100 ms; Where2comm none) | shown
RTT idle to under load | coop_2 | 5 to 10 ms to 25 to 33 ms | shown
Real outages | coop2_0828 | 3, covering 12 % of frames | shown
Still needed |  |  | 
Best-fit synthetic baseline |  | constant or Binomial delay fitted to measured | 
More passes, second site |  | rerun sim_gap.py | 
Probe-off control run |  | one run in the session | 
11/14

## Slide 12
Q6. Is it unique? Q7. Is it reproducible?
Q6 What can it do that no existing platform can?
      Setup: capability table: indoor; heterogeneous incl. infrastructure; pose reference without mocap or GNSS; every pair's link measured; CSI; clock bound reported; replay into methods; perception scoring
      Answer: SCooP-iT fills all eight columns. Nearest: CooperScene (outdoor C-V2X, no CSI, replay unknown), CoPeD (heterogeneous, estimator pose, no link)
      Lacking: verify every cell against the cited paper
Q7 Can someone else build and use it?
      Setup: bill of materials, setup effort per site, released pipeline, spec sheet with every bound
      Answer: pipeline released with the analysis tools for E1, E2, E4, E5; spec sheet drafted; component list per agent class
      Lacking: cost per agent class; mapping time, boards, control distances, software versions per site; payload node and twin_run.py
12/14

## Slide 13
Q6 and Q7 results: unique, reproducible?
Item | SCooP-iT | Nearest other / how
Answered |  | 
Indoor, no mocap or GNSS reference | yes | CoPeD (estimator pose only)
Heterogeneous incl. infrastructure | yes | CoPeD, TUMTraf-V2X
Every pair's link measured on the sensors' clock | yes | CooperScene (C-V2X, per scene)
Channel state (CSI) | yes | none
Clock bound reported; replay into methods | yes | CooperScene (PTP, no bound); AutoCast, ROS-NetSim (simulated)
Pipeline, spec sheet, component list, E1/E2/E4/E5 tools | released / drafted | Q7
Still needed |  | 
Verify every capability cell against the cited paper |  | CooperScene replay and probe rate unknown
Cost per agent class; per-site setup effort; software versions |  | bookkeeping
Payload node and twin_run.py |  | to write (Q3)
13/14

## Slide 14
Where each question stands (24 Sep)
Question | Answer now | Verdict | Still lacking
Q1 Precise | clock 0.99 ms (101x); map 0.15 / 1.06 cm; detector 8 mm; cart 3.1 cm; LiDAR robot 10 mm | pass, 2 terms short | mobile_1 on coop_2; radar; LiDAR-cam; sniffer bias; p95 speed; control distances
Q2 Consistent | rho 0.60, 5.4 dB on mobile_2 link | pass on one link | AP links; pooling; CI; out-of-run; CSI power
Q3 Faithful | model and inputs only | no data | payload node; twin-run session; comparison table
Q4 Repeatable | frame repeats: 1.06 cm, 2e-5 | half | mode distance (tool ready); repeat day
Q5 Necessary | 86 % / 59-68 % / 100 % synthetic; RTT 5-10 to 25-33 ms | shown | tuned synthetic baseline; more passes; probe-off run
Q6 Unique | all 8 capability columns | pass | verify cells
Q7 Reproducible | pipeline, tools, spec sheet, component list | partial | costs; per-site effort; payload node
Green: answered on the pre-set criterion. Orange: needs data. One field session (twin runs on the survey_1 route) closes Q3, the Q4 day half, and the sniffer bias.
14/14