## Slide 1
Digital Twin from Real Data
2/40
1 Real data one recorded pass
Scanned building
reference map, cm-level
Robots and sensors
real LiDARs, cameras, mounts
Real trajectories
where the robots drove
Measured Wi-Fi link
RTT, goodput, outages
2 Digital Twin · Isaac Sim
Comms
latency · loss · bandwidth
Sensor dropouts
LiDAR or camera off
Pose source
ground truth · noisy · SLAM
People and objects
walkers · furniture
Robot paths
new routes · speed
Sensor models
LiDAR beams · resolution
Scenario 1 4 people · 30% loss · camera off · SLAM poses
✓ sensor data ✓ GT boxes ✓ link per frame
× N
built
planned
3 Train on digital-twin scenarios
next step
4 Test on real held-out real recording
held-out real recording
Notes: Start from one real recorded pass: the scanned building, our real robots and sensor mounts, the trajectories they drove, and the Wi-Fi link we measured. The digital twin in Isaac Sim keeps all of that real and lets us change one thing at a time: the comms (latency, loss, bursts, bandwidth), sensor dropouts, where the poses come from (ground truth, noisy, or a SLAM algorithm's output), people and furniture, robot paths, and sensor models. Each setting is a scenario that comes with sensor data from every robot, ground-truth boxes for free, and the link per frame, so we can make as many training scenarios as we want. The models are then tested on a held-out real recording with its own measured link, so sim-trained and real-trained models can be compared on the same scene. Built today: comms, people and objects, robot paths, sensor models. Planned: sensor dropouts, SLAM as the pose source, and the training step itself.